## Slide 1: RX-AA (Raw Value Retrieved from [Ambient] Slot)
1 byte of UDP Number (Value 0 → 3) Indicate which part of the vertical line we are currently receiving.
An UDP packet has 1200 bytes. 4 UDP packets form
a vertical line of image.
1198 bytes of raw value. (The 4th UDP packet has 1086 bytes)
4 UDP packets with the same PSN form a vertical line on image.
Total 1198 + 1198 + 1198 + 1086 = 4680 bytes from the Ambient slot.
And every 3 bytes represent a pixel on the result image. Thus, the image will have 1560 pixels in height.
The last of the 4 UDP packets will have some trailing data just to make it 1200 bytes like the other packets.
…
PSN 0 ~ 104
Retrieve and convert the 3 bytes value to grayscale for every pixel.
The result image will be 105 x 1560 pixels.
Blue parts become 1560 pixels height
1 byte of PSN (Value 0 → 104) Indicate which vertical line we are currently receiving. (from left → right)

## Slide 2: BS-AA (Raw Value Retrieved from [Intensity] Slot)
1 byte of PSN (Value 0 → 104) Indicate a vertical line of pixels of the result image (from left → right)
An UDP packet has 1047 bytes. Due to format change, we only use the first 1041 bytes (including PSN) for now.
1040 bytes of a vertical line’s raw value from Intensity slot.
Every 2 bytes represent a pixel on the result image. Thus, the image will have 520 pixels in height.
Due to last-minute changes,
there are some unused trailing bytes.
…
PSN 0 ~ 104
Retrieve and convert the 2 bytes value to grayscale for every pixel.
The result image will be 105 x 520 pixels.
Becomes 520 pixels height

## Slide 3
520 pixels
? 520 ? * 2 bytes of pixel’s time-lapse value
A single one of these now only consist ONE vertical line of pixels of image (One slot)
105 slots
(from left to right on image)